## Slide 1: EARTH Study
(Evaluating and Assessing Radon Testing in Housing)
Michael Kitto, Principal Investigator
Calvin Murphy, Field Data Coordinator
Jonathan Wilson, Sherry Dixon, David Jacobs, National Center for Healthy Housing
Jane Malone, AARST National Policy Director
1

## Slide 2: About the EARTH Study
Three year HUD funded research project.
Looking at Multifamily testing standards and protocols
Regulating Authority | Radon testing protocol
Federal National Mortgage Assoc. (known as Fannie Mae) | 10% of ground floor units
Federal Home Loan Mortgage Corp. (known as Freddie Mac) | 10% of ground floor units
U.S. Department of Housing and Urban Development (HUD) | 25% of ground floor units
ANSI-AARST MAMF Multifamily Buildings 2017 | 100% of ground floor units
NRPP-accredited and some states require 100% of ground-floor units be tested for radon

## Slide 3: Data Requirements
Ground Floor testing results for 100% of residential units.
Seeking radon results for buildings with 5 to 20+ ground-floor units.
Looking for 30 buildings of every size (59 buildings per category).
Have much data for 5-6 and 7-8 unit buildings.
Accepting data for all categories.
Data collection ends in Dec. 2019.
September 9, 2019 3

## Slide 4
GF Units per building | Valid GF buildings
5-6 | 88
7-8 | 99
9-10 | 42
11-12 | 47
13-14 | 20
15-16 | 23
17-18 | 11
19-20 | 10
More than 20 | 29
EARTH Study data- Distribution of buildings
(The target is 59 buildings per building size category)

## Slide 5
How many units, that are all below 4 pCi/L, need to be measured so there is confidence that
fewer than 5%, 10%, 15%, 20% and 25% of units are over 4 pCi/L?
Number of GF units in building | (p=25%) | (p=20%) | (p=15%) | (p=10%) | (p=5%)
5 | 3 | 5 | 5 | 5 | 5
6 | 4 | 5 | 6 | 6 | 6
7 | 5 | 5 | 6 | 7 | 7
8 | 6 | 6 | 6 | 8 | 8
9 | 6 | 6 | 6 | 9 | 9
10 | 6 | 7 | 7 | 10 | 10
11 | 6 | 7 | 8 | 10 | 10
12 | 6 | 7 | 8 | 10 | 11
13 | 6 | 7 | 9 | 10 | 12
14 | 6 | 7 | 9 | 10 | 13
15 | 6 | 8 | 9 | 10 | 14
16 | 7 | 8 | 9 | 11 | 15
17 | 7 | 8 | 9 | 12 | 16
18 | 7 | 8 | 10 | 12 | 17
19 | 7 | 8 | 10 | 13 | 18
20 | 7 | 9 | 11 | 14 | 19
21 | 7 | 9 | 11 | 14 | 19
22 | 7 | 9 | 11 | 14 | 19
Theoretical calculations based on hypergeometric distribution.

## Slide 6
 |  | 10% sampled | 25% sampled | 50% sampled | 75% sampled
# GF units | N | Mean probability | Mean probability | Mean probability | Mean probability
05-06 | 35 | 61% | 38% | 22% | 5%
07-08 | 50 | 53% | 34% | 14% | 4%
09-10 | 27 | 61% | 34% | 20% | 7%
11-12 | 27 | 51% | 40% | 20% | 7%
13-20 | 33 | 51% | 34% | 19% | 7%
Percentage of buildings with ground-floor units containing over 4 pCi/L that
would not be found when sampling 10%, 25%, 50% or 75% of ground floor units
Quiz slide

## Slide 7
Chart: Fig 1. Five Ground floor units (n=16 buildings)
| 0 | 1 | 2 | 3 | 4 | 5
Count | 0.56 | 0.06 | 0.13 | 0.25 | 0 | 0
Chart: Fig 2. Six Ground floor units (n=72 buildings)
| 0 | 1 | 2 | 3 | 4 | 5 | 6
 | 0.61 | 0.14 | 0.14 | 0.04 | 0.06 | 0 | 0.01
7/16 buildings have units with radon >4 pCi/L
28/72 buildings have units with radon >4 pCi/L
Percentage of buildings with 5 or 6 ground-floor units containing radon > 4 pCi/L.

## Slide 8
Chart: Fig 3. Seven Ground floor units (n=32 buildings)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
 | 0.53 | 0.16 | 0.09 | 0.09 | 0 | 0.09 | 0.03 | 0
Chart: Fig 4. Eight Ground floor units (n=67 buildings)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 0.48 | 0.07 | 0.1 | 0.1 | 0.04 | 0.04 | 0.03 | 0.01 | 0.1
15/32 buildings have units with radon >4 pCi/L
34/67 buildings have units with radon >4 pCi/L
Percentage of buildings with 7 or 8 ground-floor units containing radon > 4 pCi/L.

## Slide 9
Chart: Fig 6. Ten Ground floor units (n=30 buildings)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 | 0.3 | 0.3 | 0.1 | 0 | 0.07 | 0.07 | 0 | 0.03 | 0.07 | 0 | 0.07
Chart: Fig 8. Twelve Ground floor units (n=32 buildings)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | 0.41 | 0.13 | 0.19 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0.03 | 0 | 0.06 | 0 | 0.03
As number of ground floor units increases, the probability of having a unit >4 pCi/L increases.
Percentage of buildings with 10 or 12 ground-floor units containing radon > 4 pCi/L.

## Slide 10
Conclusions
High percentage of multifamily buildings have radon below 4 pCi/L.
5-10% of buildings with at least one unit having radon over 4 pCi/L
would not be identified when 75% of the units are measured.

## Slide 11: If you have data and want to participate
Email Calvin at mfrnstudy@gmail.com or call 618-204-5545.
$2.00 per line for usable data (previously-collected or new).
As you plan to conduct future testing of multifamily buildings, contact Calvin to more easily provide data to the study.

## Slide 12
The work that provided the basis for this publication was supported by funding under cooperative agreement # NYHHU0038-17 from the U.S. Department of Housing and Urban Development’s Office of Lead Hazard Control and Healthy Homes. The substance and findings of the work are dedicated to the public. The author and publisher are solely responsible for the accuracy of the statements and interpretations contained in this presentation. Such interpretations do not necessarily reflect the views of the Government.