## Slide 1: Radon Exposure at Workplaces and Public Buildings – Experience and Future Challenges
Dr. Valeria Gruber
Radon and Radioecology, National Radon Centre of Austria
The 2017 International Radon Symposium™
Austrian Agency for Health and Food Safety (AGES)

## Slide 2: About us…
The 2017 International Radon Symposium™
Austria, Europe

## Slide 3: About us…
Radon situation in Austria
The 2017 International Radon Symposium™
Austria
USA
Population: 8.8 mio
Area: 83.879 km²
9 federal states -
Radon situation diverse
(geology dependent)
Ref.: WHO
Bq/m³

## Slide 4: About us…
The 2017 International Radon Symposium™
Embeded in the Austrian Agency for Health and Food Safety (AGES)
Financed by the Austrian Ministry of Environment
Responsible for national radon work in Austria
  Advicing MoE (implementation new EU-directive)
  Preparing and monitoring national radon action plan
  Austrian radon map, delineation of „radon areas“
  Radon awareness, risk communication, training, education
  Pilot studies on specific questions
National Radon Centre of Austria

## Slide 5: Radon and Workplaces
Current recommended levels for indoor radon concentration (since 1992):
  400 Bq/m³ action level for existing buildings (~ 11 pCi/l)
  200 Bq/m³ target level for new buildings (~ 5 pCi/l)
No legal obligation to measure radon in “general” workplaces
Obligation to measure “Workplaces with potentially elevated radon exposures” (since 2008, NatStrV)
  waterworks, underground workplaces, show mines and caves, radon spas
Future: European Basic Safety Standards (implementation by EU-MS by 2018)
  Reference level for dwellings and workplaces not higher than 300 Bq/m³ (~ 8 pCi/l)
  Obligation to measure radon in
        „General“ workplaces in basement and groundfloor rooms in „radon areas“
        Specific workplaces with potentially elevated radon exposures
Legal Background - Austria
The 2017 International Radon Symposium™

## Slide 6: Experience in Austria
General workplaces, Public buildings (no legal obligation yet)
  Kindergartens and childcare centers (~ 800; regional) – 1999-2003
  Schools (~ 350, Upper Austria) – 2002
  Administrative buildings – town halls (~ 440, Upper Austria) – 2008
Specific workplaces – Pilot studies
  Pilot study waterworks (45, Upper Austria) – 2004-2006
  Pilot study spas (3, Upper Austria) – 2005-2006
  Pilot study visitor mines and show caves (9, Austria) – 2008-2010
Specific workplaces – implementation of NatStrV („Authorized laboratory“)
  water supplies (~ 40, Austria)
  visitor mines (3, Austria)
  radon spas (~ 5, Salzburg)
Radon at workplaces and public buildings
The 2017 International Radon Symposium™

## Slide 7: „Healthy Air for Upper Austria‘s Kids“
Include Radon in Indoor Air programmes
The 2017 International Radon Symposium™
Radon
Chemical indoor parameters (formaldehyde, VOC, PCP, PCB)
Smell
Mould
Acoustics
Tightness of building, draught

## Slide 8: Results
Radon in schools
The 2017 International Radon Symposium™
Schools, control group
64 (20%) schools > 400 Bq/m³
23 (6%) schools > 1000 Bq/m³
Schools, radon areas

## Slide 9: CO2 and Radon
In schools and kindergartens
The 2017 International Radon Symposium™
During class, CO2 ↑, Radon ↓
Students in the room:
Conclusion:
Solving the CO2 problem in schools and kindergartens would (mostly) also solve the radon problem!!
CO2
Radon
Temperature
Air humidity
CO2 meter

## Slide 10: Time sensitive Radon testing
How well do continous measurements reflect radon concentration during working hours?
The 2017 International Radon Symposium™
 | Mean ratio opening hours / all day (24/7) | Variation
Kindergartens (n=50) | 0.90 | 0.27 – 2.03
Schools (n=44) | 1.20 | 0.20 – 3.72
  Mean radon concentrations reflect the radon exposure during operating hours on average quite well, however, deviations by a factor of 3 are possible (in both directions)
  Ventilation habits
  Operating hours (only mornings or all day long)
  Generally higher radon concentrations at weekends

## Slide 11: Radon in Administrative Buildings
Measurements for 6 months, passive detectors
Raising Radon Awareness for Regulators!
The 2017 International Radon Symposium™
Max. Radon concentration | Number of Buildings | %
< 400 Bq/m³ | 370 | 87
400 – 1000 Bq/m³ | 46 | 11
> 1000 Bq/m³ | 7 | 2
Measures necessary

## Slide 12: Radon in waterworks
Rn-exposed workers in Austria
The 2017 International Radon Symposium™
45 waterworks (selected according to geology and water volume)
142 measurements, active, Electret
All areas in waterworks (well houses, water storage basins, treatment facilities, offices)

## Slide 13: Radon in waterworks
Results
The 2017 International Radon Symposium™
55% < 1.000 Bq/m³
99% < 10.000 Bq/m³
Ringer, W. et al.: Mitigation of Three Water Supplies with High Radon Exposure to the Employees; Radiat Prot Dosimetry, 2008; 130 (1): 26-29

## Slide 14: Experience in waterworks
Mitigation is (usually) quite cost-effective
Identification of radon source(s) before mitigation (radon diagnosis), e.g. water treatment techniques like vaporizer, cascade etc.
No employee above 6mSv/a after some remedial measures (reduce occupancy hours in relevant building!, ventilation)
Highest doses during (annual) cleaning of reservoirs –> Measures: more workers for less time; increase ventilation; remove source!
Familiarize the workers with “radon measures” - include in work instructions, regular information and reminders
Some conclusions
The 2017 International Radon Symposium™

## Slide 15: Radon in visitor mines and show caves
6 visitor mines, 3 caves (selected by geology, raw material, number of visitors, opening hours)
active measurements for 1 year (several locations within mine/cave)
radon, thoron, equilibrium factor, air pressure, temperature
Pilot study
The 2017 International Radon Symposium™
Gruber, V., Ringer, W., Gräser, J., Aspek, W., Gschnaller, J.: Comprehensive investigation of radon exposure in Austrian tourist mines and caves, Radiat Prot Dosimetry, 162(1-2), 78-82 (2014)

## Slide 16: Examples
The 2017 International Radon Symposium™
Radon concentrations in visitor mines
Iron-ore mine, 1 year measurement
constant temperature about 8°C
Closing of gallery door during winter, to prevent cooling of the mine
Silver mine,
6 months measurement
constant temperature
about 9°C

## Slide 17: Rn concentration and doses
In mines higher than in caves
Object | Mean Rn222-conc. [Bq/m3] without winter
Show caves | 960
Salt mine | 1300
Iron ore mines | 3000
Silver mines | 4200
Copper Mine | 4900
 | mean annual dose [mSv/a]
Show caves | 0,9
Salt mine | 1,1
Iron ore mines | 1,9
Silver mines | 3,3
Copper mine | 5,4
The 2017 International Radon Symposium™
Range of average Rn-conc.:
200 – 16.000 Bq/m³
Max. conc.:
60 kBq/m³ in silver mine
Main impact factors:
Geology („mining product“)
Structure of cavities
Temperature difference
outside/inside (seasonal variations)
- Artifical ventilation

## Slide 18: The „Good Radon“
Radon spas included in legislation -> employees in radon spas controlled
Most of employees < 6 mSv/a (radon concentration not too high due to mechanical ventilation systems (moisture))
Some workers permanently controlled with personal dosimeters (> 6 mSv/a, but < 20 mSv/a) (technicians - baths, radon water treatment) – measures recommended (reduce time, tightness of doors, ventillation etc.)
Problem: Water supplies for radon spas: very high radon concentrations can occur (> 2 MBq/m³) -> cleaning of water storage basins !!!
Situation of workers in radon spas in Austria
The 2017 International Radon Symposium™

## Slide 19: Future Challenge
Reference value → 400 Bq/m³ ↓ (most probably 300 Bq/m³)
Implementation of EU-BSS for buildings with public access and „general“ workplaces
  Define „radon areas“
  „Exclude“ specific workplaces from mandatory measurements according to other criteria (e.g. mechanical ventilation system, preventive measures carried out, occupancy time, other building characteristics)
  Establish guidelines how to measure and evaluate workplaces/big buildings
  Install/promote measurement and dose evaluation services – certification, quality assurance
Carry out the mandatory radon
measurements in workplaces!
Implementation of EU Basic Safety Standards
The 2017 International Radon Symposium™

## Slide 20
Dr. Valeria Gruber
National Radon Centre Austrian Agency for Health and Food Safety (AGES) Radiation Protection
Department for Radon and Radioecology Wieningerstrasse 8 A-4020 Linz, Austria
Tel. ++43-(0)50555-41906 Fax ++43-(0)50555-41915 valeria.gruber@ages.at www.ages.at
The 2017 International Radon Symposium™
Thank you for your attention!