## Slide 1: A Comparison of Various Factors Affecting Analysis of Radon in Water by Liquid Scintillation Counting
Uttam Saha, Leticia Sonon, Michael Kitto1, Pamela R. Turner, Dana Lynch, and Gabrielle Walters
The University of Georgia Cooperative Extension, Athens, GA
1Laboratory of Inorganic & Nuclear Chemistry, Wadsworth Center, New York State Department of Health, Albany, NY
sahau@uga.edu
The 2017 International Radon Symposium™
October 1-4, 2017; New Orleans, LA, USA

## Slide 2
The 2017 International Radon Symposium™
OUTLINE
Introduction:
    Importance of Radon in Household Water Testing and Education Program.
    Rationale and objectives of this study.
Materials and Methods:
    What were the compared variables with regards to:
        Methods of Sampling, Sample Preparation, Type of Scintillation Fluids and LSC Assays?
    How those variables were created and compared.
Results: Present and Interpret.
Concluding Remarks
Questions, Comments, Suggestions

## Slide 3: Introduction
The 2017 International Radon Symposium™
How is Radon Formed?
Does it Exist in GA Well Waters?

## Slide 4: Radon in Indoor Air: Selected State Risk Estimates
The 2017 International Radon Symposium™
South Eastern United States | Radon-Induced Lung Cancer Deaths per Year | Rank
Georgia | 822 | 1
Tennessee | 693 | 2
Florida | 668 | 3
Kentucky | 600 | 4
North Carolina | 435 | 5
Alabama | 391 | 6
South Carolina | 221 | 7
Mississippi | 113 | 8
Introduction

## Slide 5: Introduction
The 2017 International Radon Symposium™
Health Effects of Radon in Drinking Water
Can Cause Both Lung and Stomach Cancer
In the US, 168 deaths are due to radon in water. Of the 168 deaths:
89% is due to lung cancer!
11% is due to stomach cancer
Action Levels
Radon in Indoor Air: 4 pCi/L
Radon in Water:
Proposed MCL: 300 pCi/L
Proposed AMCL: 4000 pCi/L

## Slide 6: Radon in Water Can Enrich Radon Level in Indoor Air
The 2017 International Radon Symposium™
A very rough rule of thumb:
Household water with 10,000 pCi/L of radon contributes about 1 pCi/L to the level of radon in the indoor air.
Introduction

## Slide 7: Introduction
The 2017 International Radon Symposium™
Radon in Indoor Air in a GA Home with:
Uranium in Water: 629 ppb
Radon in Water: 79,012 pCi/L
Radium (Ra-226+Ra-228 in Water: 3.8 pCi/L)
Health Risks from Radon in Drinking Water
Average: 5.8±0.2 pCi/L
Showering and/or Laundering

## Slide 8: Introduction
The 2017 International Radon Symposium™
The AESL-UGA launched a new Radon in Household Water Testing and Education program from August, 2015.
However, developing a proper method for “Analysis of Radon in Water” is still an important research task.
Various empirical methods of sampling, Sample preparation, Type of scintillators, Volume ratios of Scintillator : Sample, and Type counting assays on a LSC are practiced by different. laboratories testing radon in water across the United States.
Besides, there are different views regarding the effect of air-bubbles when present in the sample bottle.
The objective: Compare a selected set of these variables on the recovery of radon from:
Two “Radon in Water” standard samples, and
A few household well water samples from Georgia.

## Slide 9: MATERIALS AND METHODS
The 2017 International Radon Symposium™
4 Private Well Water Samples:
  Well-1: 6090DFR
  Well-2: 711JP
  Well-3: 715JP
  Well-4: 578TR
Three contained elevated levels of uranium.
“Well-1: 6090DFR” water revealed 629 ppb uranium, 3.8 pCi/L radium (226Ra + 228Ra), and 79,000 pCi/L radon.

## Slide 10: MATERIALS AND METHODS
The 2017 International Radon Symposium™
Well | Date | Uranium Conc. (ppb)‡ | Comment | Date | Uranium Conc. (ppb)
Well-6090DFR | 3 March, 2016† | 542 | Sampled by U. Saha | 14 June, 2011§ | 629
Well-711JP | 20 June, 2016† | 22.6 | Sampled by D. Lynch |  | 
Well-715JP | 16 June, 2016† | 407 | Sampled by U. Saha |  | 
Well-578TR | 16 June, 2016† | 4,939 | Sampled by U. Saha | 15-June, 2011§ | 1,549
Well-1: 6090DFR; Well-2: 711JPR; Well-3: 715JPR; Well-4: 578TR
Uranium Concentration in the Wells
†Sampled and analyzed as part of this study.
‡EPA’s MCL for drinking water is 30 ppb.
§Voluntary submission by the well owner.

## Slide 11: MATERIALS AND METHODS
The 2017 International Radon Symposium™
Standard Samples: 2 radon in water standard samples (or PT samples) from NYDOH

## Slide 12: MATERIALS AND METHODS
The 2017 International Radon Symposium™
Variables Compared:
Two Sampling Methods: Direct-Fill versus Submerged Bottle Method.
Two Different Scintillation Fluids: Mineral Oil versus Opti-Fluor.

## Slide 13: MATERIALS AND METHODS
The 2017 International Radon Symposium™
Variables Compared:
Two Sample Preparation Methods: “Simultaneous Drawing” versus “Separate Drawing”

## Slide 14: MATERIALS AND METHODS
The 2017 International Radon Symposium™
Variables Compared:
Two Different Volume Ratios in Making the Cocktail:
10 mL Scintillator + 10 mL Water
8 mL Scintillator + 8 mL Water
Location of Making the Cocktail:
On-site, Immediately After Sample Collection
In the Laboratory, 5-8 h (up to 24 h) After Sample Collection

## Slide 15: MATERIALS AND METHODS
The 2017 International Radon Symposium™
Two Different LSC Assays: Full spectrum (0 to 2000 keV) versus ROI of 222Rn (130-700 keV)
Regions | Assay-1 |  |  | Assay-2 | 
 | Lower Limit (keV) | Upper Limit (keV) |  | Lower Limit (keV) | Upper Limit (keV)
A | 0 | 2000 |  | 130 | 700
B | 0 | 2000 |  | 150 | 1800
C | 0 | 2000 |  | 0 | 2000

## Slide 16
The 2017 International Radon Symposium™
Effects Air Bubble: 0cc 0.5cc and 1.0cc
MATERIALS AND METHODS
Statistic: Standard Error of Duplicate Measurements for Each Contrasting Variables
Variables Compared:

## Slide 17: RESULTS
The 2017 International Radon Symposium™
Well-1: 6090DFR; Well-2: 711JPR; Well-3: 715JPR; Well-4: 578TR
Sampling Methods: Direct-Fill versus Submerged Bottle

## Slide 18: RESULTS
The 2017 International Radon Symposium™
Well-1: 6090DFR; Well-2: 711JPR; Well-3: 715JPR; Well-4: 578TR
Two Scintillation Fluids: Mineral Oil versus Opti-Fluor

## Slide 19: RESULTS
The 2017 International Radon Symposium™
Well-1: 6090DFR
Two Prep. Methods: Separate Drawing versus Simultaneous Drawing
Well-1: 6090DFR

## Slide 20: RESULTS
The 2017 International Radon Symposium™
Well-1: 6090DFR; Well-2: 711JPR; Well-3: 715JPR; Well-4: 578TR
Scintillator and Water Sample Mixed Onsite versus in the Laboratory

## Slide 21: RESULTS
The 2017 International Radon Symposium™
Well-1: 6090DFR; Well-2: 711JPR; Well-3: 715JPR; Well-4: 578TR
Volume Ratios:
Mineral Oil : Water; 10 mL : 10mL versus 8 mL : 8 mL

## Slide 22: RESULTS
The 2017 International Radon Symposium™
Volume Ratios: Opti-fluor : Water
10 mL : 10mL versus 8 mL : 8 mL
Well-1: 6090DFR

## Slide 23: RESULTS
The 2017 International Radon Symposium™
LSC Assay Types:
Assay-1 (Full Spectrum: 130-700 keV) versus Assay-2 (ROI: 130-700 keV)

## Slide 24: RESULTS
The 2017 International Radon Symposium™
Temporal Variation in Radon Concentration in 3 Wells
Well-2: 711JPR; Well-3: 715JPR; Well-4: 578TR

## Slide 25: RESULTS
The 2017 International Radon Symposium™
Well-3: 715JPR; Well-4: 578TR
Effect of Air-Bubble in the Sample

## Slide 26: RESULTS
The 2017 International Radon Symposium™
With Standard Samples
Known: 3840 pCi/L
~75% of the known: 2880 pCi/L
~125% of the known: pCi/L

## Slide 27: RESULTS
The 2017 International Radon Symposium™
With Standard Samples
8 consecutive measurements at University of Georgia laboratory
Two different LSC assays: 0-2000 keV versus 130-700 keV
Two different scintillation fluids: Mineral oil versus Opti-fluor

## Slide 28: Conclusions
The 2017 International Radon Symposium™
Sampling Methods: Direct-Fill Method is susceptible to significant Loss of Radon gas, submerged bottle method should be used.
Counting Assays: The Assay-2 (130-700 keV) is better than the full spectrum assay (0-2000 keV).
Effects of Air Bubbles: Air Bubble in the samples results in significant Loss of Radon gas; such loss becomes greater as the size of the air bubbles becomes larger.
Scintillation Fluids: Mineral oil generally gives higher radon counts than Opti-fluor. However, the results of PT or Standard samples showed that Mineral oil Clearly over estimates the actual Radon concentration, whereas Opti-oluor always gave the results close to the True value.
As a scintillator for radon in water, it is widely believed that Mineral oil is a better than Opti-fluor. However, our results show that the opposite is indeed true!

## Slide 29: Conclusions
The 2017 International Radon Symposium™
Volume Ratio: A 10 mL scintillator + 10 sample combination is better than 8 mL scintillator + 8 mL sample combination for a liquid scintillation cocktail.
Sample Prep. Method: “Separate Drawing” of scintillator and sample may result in significant loss of Radon; So, “Simultaneous Drawing” should be adopted when laboratories use open pipettes. However, this effect may be insignificant if a closed-top (no headspace) sampling syringe is used.
Making Cocktail by mixing scintillator and sample in the laboratory is better than making the cocktail on-site for both better results and practicality of testing Radon in private well waters.
There were Noticeable Temporal Variation in both radon and uranium concentrations in the study wells.
Use of uranium concentration over 30 ppb (the MCL of uranium in drinking water) as a Trigger for recommending test for radon in well water remains questionable because there may be safe level of uranium but unsafe level of radon, and vice versa in a given well water.

## Slide 30
The 2017 International Radon Symposium™
URANIUM AND RADON IN INDOOR AIR AND DRINKING WATER TESTING AND EDUCATION PROGRAM

## Slide 31
The 2017 International Radon Symposium™
UGA WATER MAP
http://aesl.ces.uga.edu/water/map/
Updated: 8/31/2017
URANIUM

## Slide 32
The 2017 International Radon Symposium™
Radon in Water:
Proposed MCL: 300 pCi/L
Proposed AMCL: 4000 pCi/L
UGA WATER MAP
http://aesl.ces.uga.edu/water/map/
RADON
Updated: 8/31/2017

## Slide 33: THANK YOU VERY MUCH!!!
The 2017 International Radon Symposium™
QUESTIONS, COMMENTS……….
Contact:
Uttam Saha, PhD
Public Service Associate & Program Coordinator
Agricultural and Environmental Services Laboratories
The University of Georgia, Athens, GA
706-542-7690
sahau@uga.edu