## Slide 1: What We Know About Uranium and Radon Household Well Waters IN Georgia
Uttam Saha, Leticia Sonon, Pamela R. Turner, Dana Lynch, and Gabrielle Dean
The University of Georgia Cooperative Extension Athens, GA
sahau@uga.edu
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Notes: This presentation is an up-to-date summary of Testing, Public Education, and Mitigation program on Uranium and Radon in Georgia well water

## Slide 2
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Introduction:
  Review the past observations made by several investigators
  History of the testing, public education, and mitigation program of University of Georgia Extension
Summary of the accomplishments so far
Concluding Remarks
Questions, Comments, Suggestions
OUTLINE
Notes: This is a brief outline of this talk.
In the Introductory part of this talk, I will Review the past observations made by several investigators
Then I will present a brief History of the testing, public education, and mitigation program of University of Georgia Extension
After that I will share the Summary of the accomplishments we made so far
Finally, I will make some Concluding Remarks
I will finish up responding to Questions, Comments, Suggestions
Let’s get started

## Slide 3
Blueridge and Piedmont Crystalline Rock Aquifer Systems in Southeastern U.S. (USGS data)
Do Uranium and Radon Exist in GA Well Waters?
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Notes: This figure shows the extent of the Blueridge and Piedmont Crystalline Rock Aquifer Systems in Southeastern U.S. You can see a significant proportion of GA has this aquifer.
The Granite bed-rock contains uranium bearing minerals, which is the source of uranium, radium, and radon in the well waters in this area

## Slide 4
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
INTRODUCTION
Radionuclides from three naturally occurring decay series headed by:
238U
230Th
235U
have long been known to be present in ground water and surface water in Georgia (Cline et al., 1983; Hess et al., 1985; Zapecza and Szabo, 1988; Coker and Olive, 1989).
Notes: Radionuclides from three naturally occurring decay series headed by:
238U
230Th
235U
have long been known to be present in ground water and surface water in Georgia .
Here are some published articles regarding this fact

## Slide 5
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
INTRODUCTION
Notes: Here are few others

## Slide 6
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
INTRODUCTION
Notes: Here is a report produced by Albertson in 2003 studying the PWS. The dark colored counties in this map are the ones that that at least one sample with greater than 30 ppb uranium.

## Slide 7
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Human Health Effects of Uranium and Radon in Drinking Water
Uranium: Drinking water with uranium levels above 30 ppb may increase the risk of kidney malfunction. Exposure to uranium in drinking water has not been shown to increase the risk of developing cancer.
Radon: Being a Class-A carcinogen, high levels of radon in drinking water can increase the likelihood of developing stomach and lung cancer.
EPA has yet to establish a federal primary drinking water standard or MCL for radon. The proposed MCL and AMCL are 300 and 4,000 pico Curies per Liter (pCi/L), respectively.
INTRODUCTION
Notes: Drinking water with uranium levels above 30 ppb may increase the risk of kidney malfunction.
However, Exposure to uranium in drinking water has not been shown to increase the risk of developing cancer.
In contrast Radon Being a Class-A carcinogen, high levels of radon in drinking water can increase the likelihood of developing stomach and lung cancer.
EPA has yet to establish a federal primary drinking water standard or MCL for radon.
The proposed MCL and AMCL are 300 and 4,000 pico Curies per Liter (pCi/L), respectively.
The Proposed MCL is 300 pCi/L means you are suggested maintain radon in water at or below 300 pCi/L, if you do not have a radon in Air mitigation device installed in your home.
The Proposed Alternate MCL is 4000 pCi/L means you can maintain radon in water at or below 4000 pCi/L, if you do have a radon in Air mitigation device installed in your home.

## Slide 8
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Human Health Effects of Uranium and Radon in Drinking Water
Across US, 180 deaths per year occur due to radon from the Public Water Supplies (PWS), of which:
      89% due to lung cancer
      11% due to stomach cancer
Number of deaths per year occur due to radon private drinking water wells is yet to be established.
INTRODUCTION
Notes: Across US, 180 deaths per year occur due to radon from the Public Water Supplies (PWS), of which:
      89% due to lung cancer
      11% due to stomach cancer
Number of deaths per year occur due to radon private drinking water wells is yet to be established, but it may be much higher because small water systems are known retain more radon than larger water systems

## Slide 9
Uranium in Drinking Water Wells: AESL Database - Pre ½ Price Program
Troup – 50.4 ppb
Fayette – 15.4 ppb
Monroe – 69.0 ppb
Oglethorpe – 62.2 & 70.7 ppb
Green - 53 ppb
Gwinnett – 26.6 ppb
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Notes: Here is how we got involved in this program.
All of this started with our Pre-2009 observation of high level of uranium in some wells, such as:
Gwinnett – 26.6 ppb
Oglethorpe – 62.2 & 70.7 ppb
Fayette – 15.4 ppb
Troup – 50.4 ppb
Green - 53 ppb
Monroe – 69.0 ppb
Especially In July 2010 – When we observed a sample exceeding Uranium MCL from A Private Well Water Sample from Monroe County.
The County Agent Discussed with Lab Personnel and Showed a Keen Interest in Extensive Testing, Public Education, Monitoring and Mitigation of Uranium in Well Waters. This discussion between the extension office and the Lab indeed laid the foundation of this whole program.

## Slide 10
The 2016 International Radon Symposium™
Communication between Extension Office (Monroe) and Trace Metals Lab, AESL, UGA
½ Price Program Initiated (As & U In Well Water Only)
Public Information Event Requested (Monroe Co.)
Community Involvement In Spreading Information
Outreach Collaboration Between Lab Group and FACS
Dana Lynch (Monroe Co.; FACS) Recognized For An ‘Outstanding Extension Program’
URANIUM AND RADON IN DRINKING WATER
Notes: Here are what happened gradually:
Communication between Extension Office (Monroe) and Trace Metals Lab, AESL, UGA
½ Price Program Initiated (As & U In Well Water Only)
Public Information Event Requested (Monroe Co.)
Community Involvement In Spreading Information
Outreach Collaboration Between Lab Group and FACS
Dana Lynch (Monroe Co.; FACS) Recognized For An ‘Outstanding Extension Program’

## Slide 11
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
The Public Service and Outreach Units collaborate and provide public education, testing, and informational resources are:
UGA Extension
  Agricultural Environmental Services Laboratories
  Monroe County
  College of Family and Consumer Sciences
Georgia Department of Public Health
U.S. Environmental Protection Agency
Monroe County Resident Donna Welch
Collaborating Partners
Notes: The Public Service and Outreach Units that collaborate and provide public education, testing, and informational resources are:
UGA Extension
  Agricultural Environmental Services Laboratories
  Monroe County
  College of Family and Consumer Sciences
Georgia Department of Public Health
U.S. Environmental Protection Agency
Monroe County Resident Donna Welch

## Slide 12
URANIUM IN DW AND RADON IN INDOOR AIR
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Notes: We conducted several Water Education Workshops most of which was in Monroe County, some in Macon county, one in High falls.
This picture is from our few workshops.

## Slide 13
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Notes: Several news casters got involved interviewing the homeowners, extension agents, and lab personnel and published news about uranium in DW wells.
Like this one published in Reporter in Forsyth, talking about ………………

## Slide 14
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Notes: This is another one published in TELEGRAPH in Macon

## Slide 15
I understand about uranium and how it could affect someone’s health. 91-94% positive response
I understand about radon and how it could affect someone’s health. 91-94% positive response
I understand what to do if I have uranium in my water. 91-94% positive response
I understand what to do if I have radon in my home. 91-94% positive response
How likely are you to use the information presented to you today? 91-94% positive response
A Program With Impact
URANIUM IN DW AND RADON IN INDOOR AIR
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Notes: The instant impact of the workshop was evaluated by inviting the attendees to answer to the 5 selected questions like.
I understand about uranium and how it could affect someone’s health. 91-94% positive response
I understand about radon and how it could affect someone’s health. 91-94% positive response
I understand what to do if I have uranium in my water. 91-94% positive response
I understand what to do if I have radon in my home. 91-94% positive response
How likely are you to use the information presented to you today? 91-94% positive response

## Slide 16
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
What We Know So Far?
Household Wells Tested | Detectable | Above MCL | Range Above MCL
Uranium (µg/L) |  |  | 
1317 | 160 | 73 | 30.1-6,297
Radon (pCi/L) |  |  | 
189 | 187 | 140 | 311-69,709
Notes: As we ran the program, we accumulated and stored the test results in our database.
Right now, our database is the most robust source of information about the emerging contaminants including Arsenic, Uranium, and Radon in DW wells in the state.
So far, we have test 1317 well waters for uranium. Of which 160 had detectable level of uranium, which are above 5 ppb. And 73 had uranium above the MCL. The range of uranium found in these 73 samples were from just over 30 ppb to as high as 6300 ppm, which is more than 200 times higher than the MCL.
Testing radon in water is a fairly new program, which we started in 2015. So far, we have test 189 well waters for uranium. Of which 187 had detectable level of uranium, which are above 100 pCi/L. And 140 had radon above the 300 pCi/L proposed MCL. The range of radon found in these 140 samples were from just over 300 pCi/L to as high as 70,000 pCi/L.

## Slide 17
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
What We Know So Far?
http://aesl.ces.uga.edu/water/map/
Notes: We developed a mapping program for uranium and radon in well waters and made it available online for public at http://aesl.ces.uga.edu/water/map/.
The mapping program updates the maps as the new results are added to the AESL database.
It allows the users to select various options and generate maps as per their choice.
This map shows the locations of the 87 wells (in yellow) that had uranium concentration at detectable (10-30 ppb) level and 73 wells (in red) that had uranium concentration higher than EPA’s Maximum Contaminant Level (>30 ppb).
This map shows the locations locations of all 111 wells (in yellow) that had radon concentration above proposed Maximum Contaminant Level (300 pCi/L) but below the proposed Alternate Maximum Contaminant Level (300-4000 pCi/L) level and 29 wells that had radon concentration higher than proposed Alternate Maximum Contaminant Level (>4000 pCi/L).

## Slide 18
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
What We Know So Far?
Temporal Variation in Radon Concentration Well Waters
Notes: Apart from evaluating the test results of uranium and radon in household well waters received from voluntary submission by the well owners, we conducted an independent study of these two contaminants in four wells namely “Well-6090DFR”, “Well-711JPR”, “Well-715JPR”, and “Well-578TR”.
When the same three wells were sampled and analyzed for radon on two different dates (28 May, 2016 and 16 June, 2016), we obtained remarkably different radon concentrations for the two different dates in any given wells (Figure (5)).
Such results suggest that temporal variation in radon concentration in the well waters is significant and should be duly considered for determining the actual overall exposure to radon from water of the household members.

## Slide 19
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
What We Know So Far?
Temporal Variation in Uranium Concentration Well Waters
Notes: Out of the four study wells, three wells (“Well-6090DFR”, “Well-715JPR”, and “Well-578TR”) had uranium concentration much higher than the EPA’s drinking water MCL. The uranium level in the “Well-711JPR” was below the MCL.
However, all four study wells had radon concentrations much higher than the EPA-proposed MCL of 300 pCi/L as well as the proposed alternate MCL (AMCL) of 4000 pCi/L.
Furthermore, the radon concentrations followed the same trend as the uranium concentrations in the wells.
Nevertheless, it is important to note here that despite there was no concern about the uranium concentration (22.6 ppb) in the “Well-711JPR”, it contained well over 20,000 pCi/L radon.
Therefore, using uranium concentration over 30 ppb as a trigger for recommending test for radon in well water remains questionable.
We also noticed temporal variation in the uranium concentration in the “Well-6090DFR” and “Well-578TR”.
Such variation was significant in the case of “Well-578TR” (1,549 ppb in June, 2001 versus 4,939 ppb in June, 2016)

## Slide 20: Radon in Water Can Enrich Radon Level in Indoor Air
A very rough rule of thumb:
Household water with 10,000 pCi/L of radon contributes about 1 pCi/L to the level of radon in the indoor air.
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Notes: We know from literature that, Radon in Water Can Enrich Radon Level in Indoor Air
And it is considered as a rough rule of thumb that Household water with 10,000 pCi/L of radon contributes about 1 pCi/L to the level of radon in the indoor air.
Through our program, we indeed have an opportunity to observe this.
This is an important observation that explains how dissolved radon in household water can contribute radon gas in indoor air

## Slide 21
Radon in Indoor Air in a GA Home with:
Uranium in Water: 629 ppb
Radon in Water: 79,012 pCi/L
Radium (Ra-226+Ra-228 in Water: 3.8 pCi/L)
Average: 5.8±0.2 pCi/L
Showering and/or Laundering
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
Notes: This is a house that had
Uranium in Water: 629 ppb
Radon in Water: 79,012 pCi/L
Radium (Ra-226+Ra-228 in Water: 3.8 pCi/L)
This graph shows the results of a WEEK LONG continuous monitoring of radon gas in indoor air.
As you can see here the average radon level was 5.8 pCi/L. But it went up to 14.4 pCi/L specially during Showering and Laundering, suggesting 8.6 pCi/L increase from the average concentration of 5.8 pCi/L (Figure (6)).
According to the well-known rule of thumb, a 79,000 pCi/L radon in household water has a potential to elevate the indoor air radon concentration by 7.9 pCi/L.
Interestingly this corresponds fairly well with the observed elevation of 8.6 pCi/L.

## Slide 22
2018 International Radon Symposium™. Sep 30 – October 4, 2018. Myrtle Beach, SC
What We Know So Far?
Community Engagement
From 2011 to the present, Monroe County Extension continues to work with state UGA Extension staff to conduct educational programs and presentations on uranium and radon. The objectives of the 1 to 3 hour programs were:
  Educate residents about uranium and radon
  Promote testing for radon in air and uranium in water
  Provide information on treatment systems
Participants Over 450
Programs 8
Print Media 159,000
Broadcast Media 60,000
Uranium tests 1303 well owners
Radon tests 170
Notes: From 2011 to the present, Monroe County Extension continues to work with state UGA Extension staff to conduct educational programs and presentations on uranium and radon. The objectives of the 1 to 3 hour programs were:
  Educate residents about uranium and radon
  Promote testing for radon in air and uranium in water
  Provide information on treatment systems
Participants Over 450
Programs 8
Print Media 159,000
Broadcast Media 60,000
Uranium tests 1303 well owners
Radon tests 170

## Slide 23: THANK YOU VERY MUCH!!!
The 2017 International Radon Symposium™
QUESTIONS, COMMENTS……….
Contact:
Uttam Saha, PhD
Public Service Associate & Program Coordinator
Agricultural and Environmental Services Laboratories
The University of Georgia, Athens, GA
706-542-7690
sahau@uga.edu